## Slide 1: TRUSS_02
Final project presentation

## Slide 2: Index
Project description
Initial model
Exploration
Exploitation

## Slide 3: Project description

## Slide 4: Project description
Geometry
  Nodal coordinates and cross-section
  Symmetry condition
  Movement permitted in y-axis for nodes at top chord
  Fixed cross-section for bottom chord
Optimize for
  Frequency / weight

## Slide 5: Project description - Bayesian optimization [1]
“Black box” function
  FEA package
Acquisition function
  Find next point of interest
Surrogate model
  Collection of all analyses
Loss function
  Scoring the model, guiding towards optimal

## Slide 6: Initial model

## Slide 7: Initial model – FEA computation implementation
Python file created for all handling with FEA package
  On initialisation – resets all previous modifications
  Updating areas and node-location
  Updating the .geom file
  Instructing FEA package for running
  Post processing FEA
  Plotting structure for ease of understanding

## Slide 8: Initial model
Bayesian package: pyGPGO
Loss function:
Acquisition function: Expected improvement
Covariance matrix: Squared exponential

## Slide 9: Initial model
Node location boundaries:
Area boundaries:
  0.1 cm2
  10 cm2

## Slide 10: Exploration
of model parameters

## Slide 11: Verifications – path to generalization
Loss function
Constrained areas
Constrained displacements
Kernel
Initial evaluations
Acquisition function

## Slide 12: Loss function
Based on the sum of following scores:
  Mass
  Natural frequency (20 Hz, 40 Hz, 60 Hz)
  Check (penalty)
Compare performance for limitations on frequency (4 scenarios)
  All frequency bands guided towards known threshold (1)
  Remove upper bound in searching optimal solution for:
    60 Hz (2)
    40 & 60 Hz (3)
    All three bands (4)
Notes: Want to talk about:
Loss function was created with regards to the score for the mass and the first three modes for the natural frequency of the structure, in addition to a penalty if the minimum threshold was breached.
We considered four initial scenarios in which: (1) all frequency bands were guided towards the known threshold of 20, 40, 60 Hz, and subsequent cases where the upper bound of the least squares function was eliminated for the listed bands on the slides

## Slide 13: Loss function – Comparison 1
 | Natural frequencies [Hz] | Best score | Total mass [kg] | Computation time [Hr] | Structure visualization for best iteration
Case 1 | 22.13, 46.83, 61.97 | 591.09 | 480.860 | 1.62 | 
Case 2 | 18.14, 50.93, 93.04 | 1511.33 | 476.760 | 3.39 | 
Case 3 | 19.40, 52.24, 66.39 | 1453.65 | 449.990 | 3.25 | 
Case 4 | 21.37, 34.19, 72.62 | 1443.04 | 443.04 | 2.55 | 
Notes: The green values represent values that achieved minimum requirements for the frequencies, while the red indicates violations.
In case (1) where all frequency bands were guided, we saw a moderate result with the most efficient computation time.
In the subsequent cases, at least one of three modal frequencies would not be met, and this is reflected in the best score with the additional penalty of 1000 points.
While the total mass was able to improve, we brainstorm additional considerations in exploring the loss function to balance, the score for the mass and natural frequency, especially with regards to the computation time since the generalization with be associated with half the level of efficiency with the same number of 500 iterations.

## Slide 14: Loss function – Additional considerations
Change the coefficient for mass score
  Optimization for all frequency bands (Case 1) with lowest C.T.
    x10 (5)
    x100 (6)
Investigate further generalization by optimizing for 20 Hz (Case 3)
  Apply combinations weights to lower bound of frequency score and the mass
    x100 frequency (7)
    x5 mass; x100 frequency (8)
    x10 mass; x100 frequency (9)
    x10 mass; x10 frequency (10)
Notes: Here are the considerations which I will delve further in the next slide with the results.

## Slide 15: Loss function – Comparison 2
 | Natural frequencies [Hz] | Best score | Total mass [kg] | Computation time [Hr] | Structure visualization for best iteration
Case 5 Same as (3) | 19.40, 52.24, 66.39 | 5884.91 | 449.99 | 3.29 | 
Case 6 | 18.14, 42.19, 63.27 | 43691.6 | 426.26 | 3.06 | 
Case 7 Same as (2) | 18.14, 50.93, 93.04 | 1822.51 | 476.76 | 3.13 | 
Case 8 | 18.27, 44.26, 79.23 | 3663.74 | 473.01 | 3.62 | 
Case 9 Same as (1) | 22.13, 46.83, 61.97 | 4808.60 | 480.86 | 3.40 | 
Case 10 | 15.92, 44.99, 74.57 | 5772.35 | 460.57 | 2.83 | 
Notes: In case 5 and 6, we optimized for the coefficient of the mass score by improving upong case where all the three modes of frequencies were guided. When optimizing for mass, we saw a great improvement in the toal mass, however, the natural frequncies would also be violated due to their natural physical relationship.
Hence, in the last four cases we seeked a combination of penalties on the mass score and frequency from case 3 where we applied the threshold guidance to only 20 Hz range in which we arrived at case 9 which was a combination of coefficient of 10 and 100 for the mass score and lower bound of frequency respectively. This ended with the same result from case, which was a great improvement in terms of generalization, however, with an associated cost for the computation time.

## Slide 16: Constraining area boundaries
The initial interval corresponds approximately to sections between CHS 21.3/2.3 and CHS 114.3/3.2. Smaller and larger intervals are tried to evaluate their influence on results and computation time.
  1: [0.00001, 0.001] for all sections
  2: [0.00005, 0.0005] for all sections
  3: [0.00001, 0.0005] for all sections
  4: [0.000005, 0.005] for all sections

## Slide 17: Constraining area boundaries
1.
2.
3.
4.

## Slide 18: Constraining area boundaries
Area boundaries | Natural Frequencies [Hz] | Total Mass [kg] | Final Score | Computation time [hr] | Structure visualization for best iteration
[0.00001, 0.001] | 22.1, 46.8, 62.0 | 480.9 | 591.09 | 2.6 | 
2. [0.00005, 0.0005] | 15.9, 44.7, 65.2 | 387.2 | 1655.66 | 2.3 | 
3. [0.00001, 0.0005] | 14.6, 49.7, 62.2 | 416.4 | 1904.34 | 3.1 | 
4. [0.000005, 0.005] | 20.7, 42.4, 61.2 | 1061.7 | 1077.20 | 3.4 | 

## Slide 19: Constraining node boundaries
Standard: Flat boundaries with 1,6 meter band
1: Flat boundaries with 1,3 meter band
2: Flat boundaries with 1,1 meter band
3: Arch shape with 1 meter band
4: Arch shape with 0,8 meter band

## Slide 20: Constraining node boundaries
1.
2.
3.
4.

## Slide 21: Constraining node boundaries
Boundaries | Natural Frequencies [Hz] | Total Mass [kg] | Final Score | Computation time [hr] | Structure visualisation
1.3 m flat | 23.8, 51.2, 77.6 | 449.5 | 1352.39 | 3.1 - 11% | 
2. 1.1 m flat | 20.5, 47.1, 70.9 | 468.3 | 806.78 | 2.6 - 26% | 
3. Arch, 1m | 22.0, 41.8, 64.7 | 510.7 | 569.80 | 1.1 - 69% | 
4. Arch, 0.8m | 23.4, 43.7, 70.1 | 475.7 | 732.79 | 1.0 - 71% | 

## Slide 22: Kernel optimization
Compare different kernels based on computation time and minimized mass:
  Squared Exponential
  Matérn
  Gamma Exponential
  Rational Quadratic

## Slide 23: Kernel optimization
Kernels | Natural Frequencies [Hz] | Total Mass [kg] | Final Score | Computation time [hr] | Structure visualisation
Squared Exponential | 14.96,46.39, 68.45 | 446.16 | 1924.96 | 1.83 | 
Matérn | 20.45, 52.50, 64.32 | 476.48 | 826.48 | 1.22 | 
Gamma Exponential | 22.13, 46.83, 61.97 | 480.86 | 591.09 | 1.74 | 
Rational Quadratic | 17.65, 42.93, 62.70 | 450.30 | 1537.44 | 2.55 | 

## Slide 24: Kernel optimization – Comparison (C.T.)

## Slide 25: Kernel optimization – Comparison (mass)

## Slide 26: Initial evaluation
Checked optimized model with
  1, 5, 10, 15, 20 Initial evaluations with FEM to feed Bayesian optimizer
  There were no apparent relationship to the total mass or final score with the use of random seed
# of initial evaluations | Natural Frequencies [Hz] | Total Mass [kg] | Final Score
1 | 27.79, 54.76, 75.83 | 480.9 | 1539.03
5 | 23.65, 55.78, 70.85 | 468.9 | 1000.58
10 | 22.13, 46.93, 61.97 | 480.9 | 591.09
15 | 20.43, 51.44, 75.09 | 501.9 | 1219.15
20 | 20.63, 49.84, 68.09 | 479.4 | 804.72

## Slide 27: Acquisition functions
Entropy (1D example) UCB (1D example)
Probability of improvement (1D example) Expected improvement (1D example)

## Slide 28: Acquisition function: Entropy and UCB
Potential good results
UCB faster convergence compared to Entropy
Both gave errors
500 iterations: 10+ hours
Entropy 1D example UCB 1D example

## Slide 29: Acquisition function: Probability Improvement
Good loss score
Faster run time
Same reward regardless of the size of the improvement of a new found maximum
Can get stuck on a local optimum
Natural frequencies [Hz] | Best score | Total mass [kg] | Computation time [Hr] | Structure visualization for best iteration
20.14, 49.65, 60.99 | 670.69 | 482.320 | 2.33 | 
P.o.I. 1D example

## Slide 30: Acquisition function: Expected Improvement
Comparebale to PoI, but is better at discovering global optimum
Good run time
Good results
Hyperparameter: ξ
Natural frequencies [Hz] | Best score | Total mass [kg] | Computation time [Hr] | Structure visualization for best iteration
20.63, 49.84, 68.09 | 804.72 | 479.43 | 2.57 | 

## Slide 31: Acquisition function: Trade-off parameter ξ [6]
Low ξ (1D example) High ξ (1D example)

## Slide 32: Acquisition function: Expected Improvement
 | Natural frequencies [Hz] | Best score | Total mass [kg] | Computation time [Hr] | Structure visualization for best iteration
High ξ | 19.42, 44.94, 60.23 | 1493.53 | 444.37 | 2.89 | 
Low ξ | 20.14, 49.65, 60.99 | 804.72 | 479.43 | 2.57 | 

## Slide 33: Exploitation
of the final model

## Slide 34: Final model
Optimized parameters:
Loss-function: Least squares for all frequencies
Acquisition function: Expected Improvement (ξ = 0)
Area bound: [0.00001, 0.001]
Node bound: [0.6, 2.2]
Kernel: Matern
Iterations: Up to 3000

## Slide 35: Final model: Issues
Problem: computational time vs. remaining time frame
Also prone to errors: GoogleColab
1500 iterations took more than 18 hours.
3000 estimated to several days

## Slide 36: Final model: Optimization
Solution:
Run multiple models of 500 iterations sequentially
Use the results from the first model as boundaries for the second model
Repeat until a satisfying solution has been found

## Slide 37: Final model: Results
Run | Natural Frequencies [Hz] | Total Mass [kg] | Final Score | Computation time [hr] | Structure visualisation
1 | 20.62, 49.83, 68.09 | 438.31 | 804.72 | 0.71 | 
2 | 21.23, 42.38, 60.51 | 471.28 | 479.87 | 0.69 | 
3 | 20.44, 40.70, 60.92 | 477.16 | 461.95 | 0.82 | 
4 | 21.30, 40.29, 60.27 | 455.62 | 461.87 | 0.70 | 
5 | 20.17, 40.94, 61.52 | 450.13 | 465.02 | 0.75 | 
6 | 20.41, 42.16, 61.28 | 455.80 | 467.69 | 0.8 | 
7 | 20.33, 40.21, 60.65 | 447.95 | 456.13 | 0.77 | 

## Slide 38: Discussion: Final model
Pros:
  Decreased computational time
  Better solution
Cons:
  Losing a lot of information gained by the Bayesian model
  Potential of taking a local optimum as boundary for next model

## Slide 39: Discussion: Bayesian optimization
Optimal truss design
  Kanarachos: ~360 kg
  Only eigen frequencies and mass
  Too low mass penalty, optimizing towards low frequencies
Suitability of Bayesian optimization
  Preliminary screening
  Efficient in reaching optimal solution
  Recurrent, non-parametric model
Generality versus computation time
  The more general the model, the more computation time needed

## Slide 40: Sources
Nag, A. (2022, 6 januari). Bayesian Optimization: A Step by step approach - towards data science. Medium. https://towardsdatascience.com/bayesian-optimization-a-step-by-step-approach-a1cb678dd2ec
Opt.Vink, R. (2019, 25 augustus). Algorithm Breakdown: Bayesian Optimization. Ritchievink. https://www.ritchievink.com/blog/2019/08/25/algorithm-breakdown-bayesian-optimization/
Kanarachos, S., Griffin, J., & Fitzpatrick, M. E. (2017). Efficient truss optimization using the contrast-based fruit fly optimization algorithm. Computers & Structures, 182, 137–148. https://doi.org/10.1016/j.compstruc.2016.11.005
Acquisition function animations: https://github.com/josejimenezluna/pyGPGO/blob/master/examples/example1d.py
Shahriari, B., Swersky, K., Wang, Z., Adams, R. P., & De Freitas, N. (2016). Taking the human out of the loop: A review of Bayesian optimization. Proceedings of the IEEE. http://doi.org/10.1109/JPROC.2015.2494218
Bayesian optimization - Martin Krasser’s Blog. (2018, March 21). https://krasserm.github.io/2018/03/21/bayesian-optimization/